## Slide 1
ENGINEERING REPORT |  | Reviewer/Team(Development) | Review Date | Approval | Issue Owner | PL | Team Leader
 |  | Terrence / TV Development MEMC Team | 2010.01.29 |  | Andy_chen/jimmy_wei | James Park /Cavin Huang | Jeffrey
1.DQA MM/ Test Cause | PQ/Claim | 2.Date of Occurrence | 2018.12.14 | 3.Title(Issue Description) | helicopter wing broken |  | 
4. Model Name (Product Family) | K5LP ( TV ) | 5. Event | SW Verification/ SW Qualification / MP | 6. Test Item / Place of Occurrence | PQ/QA | 7.Total Occurrence | 2 100%
8.Statistical Verification | No | 9.Reason for not verifying statistics | SW issues that can pass/fail without statistical significance |  |  |  | 
[Issue Description] |  | [Causes] |  |  | [Measures] |  | 
■ Issue Description helicopter wing broken ■ Key Quality Characteristics : Spec : MEMC / MC off / fall back ■ Reproduction Mode/Frequency: Pattern:CMR_xmen_apocalypse.mp4 TV :picture mode : standard mode Frequency : always |  | ■ 5-Why Description (Need to be described with objectivity and depth) |  |  | ■ Improvement Measures(Temporary/Fundamental Measures) Modify the threshold and let the broken frame enter into Global fallback |  | 
 |  |  |  |  | ■ Improved Result - Total Occurrence after improvement : 0%(10/10 OK) broken is disappear. |  | 
 |  |  |  |  | ■ Improvement Reflected Date : 2019.1.28 |  | 
 |  |  |  |  | ■ Side effect Verification - N/A |  | 
 |  |  |  |  | ■ Preventive Measures When mv is messy, current frame need enter to Global full back |  | 
■ Test Result(Current Level) - Occurrence Rate before Improvement: 100 |  |  |  |  |  |  | 
 |  |  |  |  | ■ Horizontal Deployment - N/A |  | 
Why1 | * W : motion video is broken. MEMC off is OK → W1 : ME or MC problem
Why2 | * ME or MC problem, check MC module. → W2 : Disable MC function is better
Why3 | * Show mv mode, the mv on the area of broken is messy → W3 : why is the mv messy ?
Why4 | * only disable ME function ,use original source the broken will gone. → W4 :only disable ME function ,use original source the broken will gone.
Why5 | * if the frame mv is messy, It’s keep original source is better. ->W5 : Determine these special pattern, and let the frame enter to Global fallback.
Root Cause | Because the wing move complexly, the mv is messy. so sometimes will use wrong mv data to interpolation, we will se the broken video.

## Slide 2: Review Result Report
Project | webOS 4.5 | Event | PV |  | Review Date | 2018.XX.XX
Review Title | [KTASKWBS-10129][MEMC]improve propeller broken |  |  |  | Review Item | □ Document □ Source Code
Review Document/ Source Code |  |  | Author |  | Reviewer | 
https://swfarmhub.lge.com:8100/#/c/41479/ |  |  | Andy_chen/Jimmy_wei |  | Jerry/Terrence | 
Key Changes | Fixed broken video when pure video input |  |  |  |  | 
Expected Side Effect |  |  |  | Action |  | 
Some frame may enter to local full back wrongly, and the frame may occur sudden broken. |  |  |  | Action result per each Side Effect item N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A N/A |  | 
A – 1/3

## Slide 3
Test Item | Test Script | Expected Result | Owner | Test Result
MEMC Test | Check Internal signal of PS/DIL | No broken video |  | OK
Test Result Report
A – 2/3

## Slide 4
Source Code Changes
A – 3/3
Before/After Changes Source Code diff capture
Firmware will detect current frame’s characteristic value, the characteristic value is composed of y/hue histogram flag \frame detail info\still frame flag. When current frame’s characteristic value is within the threshold range , Firmware will Modify the threshold and let the broken frame enter into Global fallback.